## Slide 1
Microprocessor Design
TAs: Sebastian Giraldo, Nathan Laubeuf,
Jasper Marien, Linyan Mei, Giuseppe Sarda

## Slide 2
Outline
Intro (support platforms)
Objectives of the sessions
Tools used
Architecture
Loading Programs
Exercises

## Slide 3: Communication platform – Discord server
On the server you can find:
Useful resources
A dedicated channels for each group
Dedicated rooms for communication with TAs
Ticketing system to ask for help from TAs

## Slide 4: Keep your project safe!
We highly suggest you to use git as a versioning tool.
It helps you to:
                keep track of modifications
                automatically sync the project between group members
                allow TAs to support you more easily
Please have a look on the dedicated guide.

## Slide 5
Objective
Design a microprocessor in RTL (Verilog) using 32 nm technology
Evaluate different microarchitectures
  Single Cycle Processor
  Single Cycle Processor (Multiplication Support)
  Pipelined Processor (without data-hazard resolution)
  Pipelined Processor (with data-hazard resolution)
Compare
  Performance
  Hardware Resources

## Slide 6
Objective
Single Cycle Processor
Single Cycle Processor (Multiplication Hardware)
Pipelined Processor
Pipelined Processor (Data-Hazard resolution)
SIMULATION + SYNTHESIS
Single Cycle Processor (Not Functional)
reports
Comparison of Microarchitectures
RISCV processor
(Optional technique)
Optional:

## Slide 7
Tools used
Simulation: NC Verilog (Cadence)
“Check the correctness of the hardware description implemented”
Synthesis: Design Vision (Synopsys)
“Convert a hardware description into physical gates”

## Slide 8
Tools used: Simulation
Hdl files
Testbench (cpu_tb.v)
NC Verilog
Simulation Results
Script to be loaded: incisiv_15.20.058.rc
Command used: make nc_gui or make nc

## Slide 9
Tools used: Synthesis
Design Vision
HDL files
Constraints (sdc)
Libraries (lib)
Netlist
Area/Timing/Power Reports
Scripts to load tool: synopsys_2017.09.rc
Command used: source synthesis.sh

## Slide 10
Architecture Used
Single Cycle Processor

## Slide 11
Architecture Used
cpu_tb
cpu
program_
counter
instruction_
memory
control_unit
register_file
alu_ctrl
alu
branch_unit
data_memory
regfile_dest_mux
alu_operand_mux
regfile_data_mux

## Slide 12
Architecture Used
Control_unit
File: control.v

## Slide 13
Architecture Used
register_file
File: register_file.v

## Slide 14
Architecture Used
program_counter
File: pc.v
(Be careful, there is
more logic)

## Slide 15
Architecture Used
branch_unit
File: branch_unit.v

## Slide 16
Architecture Used
alu
File: alu.v

## Slide 17
Architecture Used
alu_ctrl
File: alu_control.v

## Slide 18
Architecture Used
Instruction memory
File: sram.v
Data Memory
File: sram.v

## Slide 19
Architecture Used
Regfile_data_mux File: mux_2.v
Alu_operand_mux File: mux_2.v
Regfile_dest_mux File:mux_2.v

## Slide 20
Programs
MIPS language
2 extra instructions
  NOP (opcode: 111111)
  STOP (opcode: 111110)
5 programs
  Simple_program
  MULT1
  MULT2
  MULT3
  OPTIONAL4
How to load a program?
  Go to SIM/data and modify
    Imem_content.txt
    Dmem_content.txt

## Slide 21
Programs
Functions of Testbench (cpu_tb.v)
Design Vision
Loading Data Memory
Design Vision
Loading Instr. Memory
Check
Execution
Start of Program
End
of Program
CPU
Stimulation Logic
cpu_tb
dmem_content
imem_content

## Slide 22
Programs
addi $s0, $0, 7
addi $s1, $s0, 2
sw $s1, 0($0)
lw $s2, 0($0)
add $s3, $s0, $s2
beq $s1,$s2, FINAL
add $s4, $s0, $s1
FINAL: add $s5, $s2,$s3
simple_program

## Slide 23
Programs
When there is no hardware support: Mult1
1 1 0
X 1 0 1
1 1 0
0 0 0
1 1 0
1 1 1 1 0
The same as the Sum of:
110 (Shifting “110” by 0 positions)
0000 (Shifting “000” by 1 position)
11000 (Shifting “110” by 2 positions)
Algorithm:
Acc = 0
N = operand1
Traverse each bit of operand2 (LSB -> MSB)
  If the bit of operand2 is 1, accumulate. Acc = Acc + N.
  If the bit is 0, Acc = Acc.
  Left shift N by 1 position.

## Slide 24
Programs
addi $16,$0,40
addi $8, $0, 0
addi $9, $0, 0
M1:lw $17, 0($8)
lw $18, 4($8)
addi $23, $0, 32
addi $19, $0, 1
addi $20, $0, 0
add $22, $0, $17
LOOP_0: and $21, $18, $19
beq $21, $0, SHIFTING_0
MULT1
It makes 5 multiplications with 10 integers.
The results are summed together.
** Based on sums and shifts
add $20, $20, $22
SHIFTING_0: sll $22, $22, 1
sll $19, $19, 1
addi $23,$23,-1
beq $23, $0, M2
j LOOP_0
M2: add $9, $9, $20
addi $16, $16, -8
addi $8, $8, 8
beq $16, $0, FINISH
j M1
FINISH:
Data Memory
1
2
3
4
5
6
7
8
9
a
Instr. Memory
$16: Total size of data memory
$8: Data Memory Pointer
$23: Iteration over the number of bits
$20: Accumulated result of each multiplication
$9: Final result

## Slide 25
Programs
lw $8, 0($0)
lw $9, 4($0)
lw $10, 8($0)
lw $11, 12($0)
lw $12, 16($0)
lw $13, 20($0)
lw $14, 24($0)
lw $15, 28($0)
lw $16, 32($0)
lw $17, 36($0)
MULT2
** Use of mult instruction
Addi $23, $0, 0
nop
nop
nop
Add $23, $23, $18
nop
nop
nop
Add $23, $23, $19
nop
nop
nop
Add $23, $23, $20
nop
nop
nop
Add $23, $23,$21
nop
nop
nop
add $23, $23,$22
Instr. Memory
Data Memory
1
2
3
4
5
6
7
8
9
a
mult $18, $8,$9
mult $19, $10, $11
mult $20, $12, $13
mult $21, $14, $15
mult $22, $16, $17

## Slide 26
Programs
lw $8, 0($0)
lw $9, 4($0)
lw $10, 8($0)
lw $11, 12($0)
lw $12, 16($0)
lw $13, 20($0)
lw $14, 24($0)
lw $15, 28($0)
lw $16, 32($0)
lw $17, 36($0)
MULT3
** Use of mult instruction
** No NOPS between
Data-dependent
instructions
Addi $23, $0, 0
Add $23, $23, $18
Add $23, $23, $19
Add $23, $23, $20
Add $23, $23,$21
add $23, $23,$22
Instr. Memory
Data Memory
1
2
3
4
5
6
7
8
9
a
mult $18, $8,$9
mult $19, $10, $11
mult $20, $12, $13
mult $21, $14, $15
mult $22, $16, $17

## Slide 27
Exercise
Session 1:
      Complete Single Cycle Processor
      Add support for Multiplication
Session 2:
      Pipelined Processor (without data-hazard resolution)
Session 3:
      Pipelined Processor (with data-hazard resolution)
Optional Exercise:
    Porting the code to support RISC-V ISA
      (a dedicated presentation will be provided)

## Slide 28
REMARKS
The assignments must be completed in groups of 2 people.
Important: Make sure at least one student in a group has Verilog experience.
After completing each one of the exercises, the results must be shown to the TAs for its correspondent evaluation.
The code must be delivered to the TAs in the final session.
Also you will hand in a small report based on the template that you find in the folder. Together with the performance of your final processor, this counts for 2 points in the final H05d3A grade.
This report should be handed in through Toledo. The deadline will be set and communicated to you.